## Slide 2: Stomata
Definition
  Stomata are tiny openings or pores in plant tissue that allow for gas exchange (CO2, H2O…).

## Slide 3
Stomatal traits vary between species
The eudicots (A) Arabidopsis thaliana; (B) Phaseolus vulgaris; (C) Oryza sativa; (D) Triticum aestivum
dumbbell-shaped guard cells (solid green) and specialized subsidiary cells (light green gradient).
Clear differences in stomatal size and stomatal density can be observed [1]
[1]: Bertolino L T, Caine R S, Gray J E. Impact of stomatal density and morphology on water-use efficiency in a changing world[J]. Frontiers in plant science, 2019, 10: 225.

## Slide 4
Functions [1]
  Exchange the gases by closing and opening the pores in the leaves.
    Removes oxygen and takes in carbon dioxide at the time of photosynthesis.
  Assists in eradicating excess water from the leaves. (water exchange)
  Assists in monitoring the movement of water via transpiration.
Play a significant role in photosynthesis and transpiration [2-3]
[1]: Melotto M, etc. Role of stomata in plant innate immunity and foliar bacterial diseases.
Annu Rev Phytopathol.
[2]: Lawson T, etc, photosynthesis and plant water use efficiency[J]. New Phytologist, 2019.
[3]: Tuzet, A.J. Stomatal Conductance, Photosynthesis, and Transpiration, Modeling. Encyclopedia of Agrophysics.
Encyclopedia of Earth Sciences Series. Springer,

## Slide 5
Driving the water cycle, refer to [1]
[1]: Hetherington A M, etc. The role of stomata in sensing and driving environmental change[J].
Nature, 2003, 424(6951): 901-908.

## Slide 6: Stomata conductance
Stomata dynamics---open and close
Stomata are constituted by two cells : Guard cells.
Guard cells are hydraulic valves making possible stomata closure and opening.

## Slide 7: Stomata conductance
Definition
  Stomatal conductance (gs) is the diffusion of gas, such as carbon dioxide, water vapor, and oxygen, through the stomata of a plant.
Importance of measuring
  Estimates the rate of gas exchange (i.e., carbon dioxide uptake) and transpiration (i.e., water loss) through the leaf stomata as determined by the degree of stomatal aperture (and therefore the physical resistances to the movement of gases between the air and the interior of the leaf).[1]
[1]: Cotthem, Willem Van (2018-01-30). "Stomatal conductance". PLANT STOMATA ENCYCLOPEDIA

## Slide 8: Stomata conductance
Influences
  Internal Influences: plant-level factors
    Signals from the guard cell and stomatal density
    Changes in leaf water potential
    Need to take in CO2 for photosynthesis
    Etc.
  External Influences: Environmental factors
    Light is the primary external factor that determines stomatal conductance, as stomata are activated and open during daylight.
    Air temperature rises will increase stomatal conductance, independent of plant water status and photosynthesis.
    Elevated atmospheric CO2 concentration decreases stomatal conductance, which can end up reducing photosynthesis.
    Humidity influences stomatal conductance. Low humidity reduces stomatal conductance to preserve water. Stomata will open in high humidity even if the leaf water content is less.
    Etc.

## Slide 9: Stomata conductance measure method
Steady-state porometers: A steady state porometer measures stomatal conductance using a sensor head with a fixed diffusion path to the leaf. It measures the vapor concentration at two different locations in the diffusion path. (e.g., Decagon: SC-1)

## Slide 10: Stomata conductance measure method
Dynamic Diffusion– measures the rate of RH increase in a chamber clamped to the leaf surface. (e.g., Delta-T Device: AP4)

## Slide 11: Stomata conductance measure method
Viscous or Mass Flow– measures the time (in 1/100th of a second) to force a fixed volume of pressurized air through the leaf. (e.g., Thermoline)

## Slide 12: Stomata conductance measure method.
Null Balance – measures the vapor fl ux and vapor gradient near the leaf surface by calculati ng the fl ow rate needed to keep stable RH inside the chamber (including air and leaf temperature). (e.g., LICOR: LI-1600)

## Slide 13: Modeling the stomata dynamic process
Our purpose: Measure the dynamic activities of stomata opening process
What we need to measure?
  relative humidity
  Light intensity
  Keep other conditions unchanged

## Slide 14: Measurement instrument
Basic structures

## Slide 15
Structure

## Slide 16: Measurement instrument
Basic structures

## Slide 17: Measurement instrument
Measurement procedure
  Dark preprocessing (around 12 mins)
  Press the chamber on leaf surface
  Turn off the light (1 hour)
  Turn on the light and lift the chamber

## Slide 18: Technique details
Arduino board
  We use Mega 2560
  Getting start: https://docs.arduino.cc/software/ide-v1/tutorials/getting-started/cores/arduino-avr

## Slide 19: Technique details
Pinout & data sheet: https://docs.arduino.cc/hardware/mega-2560
Tutorials docs: https://docs.arduino.cc/tutorials/
Tutorials from Paul McWhorter (Video): https://www.youtube.com/@paulmcwhorter

## Slide 20: Technique details
Sensors
  Humidity sensor -TI HDC-2080
    User guide https://www.ti.com/product/HDC2080?utm_source=google&utm_medium=cpc&utm_campaign=asc-null-null-gpn_en-cpc-pf-google-tw&utm_content=hdc2080&ds_k=&dcm=yes
    HDC2080EVM module : https://www.ti.com/tool/HDC2080EVM (includes user guide, applications, etc.)

## Slide 21: Technique details
Sensors
  Light sensor --- TSL2591
    Docs & code: https://learn.adafruit.com/adafruit-tsl2591/overview
  Servo actuator --- PA-12-10645012R
    Docs : https://www.progressiveautomations.com/products/micro-servo-actuator-rs485

## Slide 24
Tube
Stage
Tobacco
Arduino

## Slide 25
D = 5mm
d = 52 mm
L = 300 mm

## Slide 26
Integrated development environment
Attention!
At least one PC with windows!

## Slide 28
5 sensors: I2C multiplexer, humidity sensor, Light sensor, SD card read/write block, Solid moisture sensor

## Slide 29: Procedure of development in Arduino IDE
Look up the type of the sensor
Take a look at the technique document
Install the corresponding library in IDE
Find the example code
Write your own code

## Slide 30: Procedure of development in Arduino IDE
Look up the type of the sensor ( Take a look at the sensor)

## Slide 31
Take a look at the technique document

## Slide 32: Install the corresponding library in IDE
Tools->Manage libraries

## Slide 33
Search ‘Light sensor’

## Slide 34: Find the example code

## Slide 35: Read the code

## Slide 36: Write your own code
Download to the board